NorCal Keyer Function Table - Keypress Combinations

| Keys Used | PAR (press and release) | PAH (press and hold) |
| --- | --- | --- |
| Mem switch | Send memory 3 | Record memory 3, O? Beacons: BE and BA |
| Mem + dit | Send speed | Paddle set of speed, pot options, main menu |
| Mem + dah | Send memory 2 | Record memory 2: M? |
| Mem + both | Send memory 1 | Record memory 1: T? |

NorCal Keyer Menus

| CW | Menu Item | Pressing a dit | Pressing a dah |
| --- | --- | --- | --- |
| Memory + Dit Menu (PAR mem to advance to the next menu) |
| S | Speed set from paddle | Increase speed 1 wpm | Decrease speed 1 wpm |
| P | Pot / paddle speed control | Selects pot speed control | Selects paddle speed control |
| C | Calibrate pot speed control | Enters the calibration routine | Restores default pot calibration |
| B | Bug / straight key mode | Enables bug mode (dah = key) | Disables bug mode (default) |
| A | Iambic mode A or B | Enables iambic mode A | Enables mode B (default) |
| R | Reverse paddle mode | Reverse dit and dah switches | Returns dit and dah to normal |
| AU | Autospace on / off | Turns on character autospace | Turns off autospace (default) |
| Memory + Dah Menu (PAR mem to exit) |
| M? | Record memory 2 | Records a dit | Records a dah |
| Memory Switch Menu (PAR mem to advance to next menu) |
| O? | Record memory 3 | Records a dit | Records a dah |
| BE | Beacon mode - sends mem 1 | Starts the beacon going | Exits the menu |
| BA | Beacon alternate mode | Selects alternate beacon sends of mem 1 and mem 2 | Selects send of mem 1 only (default) |
| ST | Side tone on/off | Turns off the side tone | Turns the side tone on |
| Memory + Both Menu (PAR mem to exit) |
| T? | Record memory 1 | Records a dit | Records a dah |

Add spaces in text strings using the space character di dah dah dah dit. The
spaces are not transmitted. Useful for delays in beacon messages etc.

W5USJ 06/10/03